## Slide 1
bioinformatics.ca
bioinformaticsdotca.github.io

## Slide 3: Module #1a: Intro to Sequencing Technologies
Dr. Erin Pleasance
CBW High-Throughput Genomics
November 4-6, 2026
Some slides adapted from Jared Simpson and previous instructors

## Slide 4: Learning Objectives
Sequencing trends
Understand the technology behind Illumina, Nanopore and PacBio sequencing
Compare and contrast the approaches
Be aware of newer technologies becoming available
Understand basic sequencing reads and quality measures

## Slide 5: DNA sequencing history
https://www.criver.com/eureka/history-dna-sequencing
Newer technologies competing in short-read space:
2022
AVITI (Element Biosciences)
2023
Complete Genomics
2024
Ultima

## Slide 6: Throughput and cost
Human genome project complete
1,000 genomes project complete
100,000 genomes project complete
https://www.fiosgenomics.com/genomics-sequencing-data-analysis-a-cost-timeline/
PMID: 37508427
All Of Us /
1+ Million Genomes

## Slide 7: Established players in sequencing
Illumina
Oxford Nanopore
PacBio

## Slide 8: DNA sequencing: DNA polymerase

## Slide 9: Illumina sequencing by synthesis

## Slide 10: Illumina sequencing by synthesis

## Slide 11: Illumina sequencing by synthesis

## Slide 12: Illumina sequencing by synthesis

## Slide 13: Homopolymers are tricky to sequence
Polymerases can slip on long sequences of the same nucleotide
Get lots of indels

## Slide 14: Illumina read profile
Read pairs facing inwards
Length usually 150 bp each end of pair
Accuracy > 99.9%
Only ACTG, no modified bases

## Slide 15: Illumina summary
High throughput, high accuracy, low cost
Different platforms for different needs
Most commonly used technology
Read length limited to ~150 bp each pair
No base modifications read
NovaSeq X Plus
MiSeq i100

## Slide 16: Oxford Nanopore (ONT) sequencing
Unique nanopore technology
Not sequencing by synthesis
https://nanoporetech.com/platform/technology

## Slide 17: Oxford Nanopore sequencing
Native DNA or RNA
No amplification
Size selection not necessary
PMID: 32504078

## Slide 18: Oxford Nanopore sequencing
Motor protein moves DNA through the pore
Detect changes in electrical signal depending on sequence in the pore (“squiggle”)
PMID: 32504078

## Slide 19: Oxford Nanopore sequencing
Signal depends on multiple bases
Basecaller decodes
https://nanoporetech.com/platform/technology

## Slide 20: Oxford Nanopore sequencing
Includes base modifications:
  5mC in DNA
  m6A in RNA
  Others with variable accuracy
PMID: 31602005

## Slide 21: Oxford Nanopore read profile
Single end
Very long reads (10 kb – 1M+)
Higher error rate especially at homopolymers
Captures base modifications
PMID: 32504078
https://nanoporetech.com/platform/technology

## Slide 22: Oxford Nanopore summary
Very long reads
Lower accuracy
Minimal prep, highly flexible
PromethION
MinION

## Slide 23: Pacific Biosciences HiFi sequencing
Create circular template
https://www.pacb.com/technology/hifi-sequencing/how-it-works/

## Slide 24: Pacific Biosciences HiFi sequencing
Millions of nanowells (Zero-Mode Waveguide, ZMW)
One polymerase each
Sequencing by synthesis
PMID: 32504078

## Slide 25: Pacific Biosciences HiFi sequencing
PMID: 32504078
Create circular template
Millions of nanowells (Zero-Mode Waveguide, ZMW)
One polymerase each
Sequencing by synthesis
Detect light emitted in nucleotide incorporation

## Slide 26: Pacific Biosciences HiFi sequencing
https://www.pacb.com/technology/hifi-sequencing/how-it-works/
Sequence repeatedly around circle and take consensus
Individual accuracy < 90%
Consensus accuracy > 99.9%

## Slide 27: PacBio read profile
Single end
Long reads (> 10 kb)
Extremely low error rate
Captures base modifications

## Slide 28: PacBio summary
Very high accuracy, long reads
Widely used for genome assembly
Higher cost per base
Large footprint
Revio

## Slide 29: Newer technologies: Ultima
Short read sequencing by synthesis
Wafer chip
Reduced use of expensive labelled dNTPs
Recently released paired reads
Pushing for $80 whole genome
https://www.biorxiv.org/content/10.1101/2022.05.29.493900v4.full

## Slide 30: Newer technologies: AVITI
Polymerase based
Multivalent nucleotide binding
Better homopolymer accuracy
Paired short reads
Not cheaper

## Slide 31: Sequencing formats
FASTA: Base sequences
FASTQ: Base sequences and quality scores
BAM/CRAM: Alignment formats (compared to a reference)
>chromosome1
AGTCGATCGATCAGACTAACGATCGATCGAATCGAAT
>chromosome1
AGTCGATCGATCAGACTAACGATCGATCGAATCGAAT
+
CFHIGIGIJIIJFHIJJIIJIHFFFEDDDDDDDDDDD

## Slide 32: Sequencing quality
Quality is measured by the Phred score (named after software Phred, used for Sanger sequencing analysis in the 1990s). Eg a “Q40 base” is highly accurate
P
(obs. base)
50 % 32 % 10 %
1 % 0.1 % 0.01 %
Base Quality 3
5
10
20
30
40
ASCII Character $
&
+
5
?
I
error
Q = -10log10Perror

## Slide 33: Representing aligned reads
Mapping/aligning reads to a reference genome is a core component of many analysis workﬂows. You’ll hear more about this in later Modules
Mapping describes where in the reference genome a read matches. This read maps to position 1,020 on chr10
Alignment describes how the bases in the read line up against the reference genome at the mapped location. This read has 14 matches and 1 mismatch.
The location of the read on the reference genome and pattern of mismatches/indels is represented in bam/cram format.
ATGAGAGAGTATCTCGACTCTAGGCCGATACCA
||||||||||||||| AGTAACTCGACTCTA
read-a
chr10:1,020

## Slide 34: Mapping quality
Mapping quality is dependent on the similarity of the match and the uniqueness of the match
More likely to be low in repetitive regions
Also uses a Phred score
Single mapping location →
Good mapping quality, if few mismatches
Multi-mapped read →
Poor mapping quality (MQ0)
https://hbctraining.github.io/

## Slide 35: We have a lot of tools

## Slide 36: Coffee Break & Networking Session
Workshop Sponsors